## Slide 1: Significant Recent Updates to IPP
Smith Kennedy – HP Inc.
PWG Vice-Chair / PWG Liaison to Mopria Alliance
2023-10-30

## Slide 2: IPP Workgroup Efforts 2020-2023
Several core IPP extension specifications "reopened"
  Resolve errata
  Re-factor individual specifications to focus on particular domains
  Support new use cases and better support existing use cases
IPP Everywhere v2.0 development also underway; many of these new features are important to that effort

## Slide 3: Recent IPP Specification Updates
PWG 5100.1-2022: IPP Finishings 3.0 (FIN)
PWG 5100.3-2023: IPP Production Printing Extensions v2.0 (PPX)
PWG 5100.7-2023: IPP Job Extensions v2.1 (JOBEXT)
PWG 5100.11-2023: IPP: Enterprise Printing Extensions v2.0 (EPX)
PWG 5100.13-2023: IPP Driver Replacement Extensions v2.0 (NODRIVER)
PWG 5101.1-2023: PWG Media Standardized Names v2.1 (MSN)

## Slide 4: IPP Specifications - Overview
IETF STD 92: IPP/1.1 (RFC 8010 and RFC 8011)
IETF RFC 7472: IPP over HTTPS Transport Binding and the ’ipps’ URI Scheme
PWG 5100.12-2015: IPP Version 2.0, 2.1, and 2.2
PWG 5100.1-2022: IPP Finishings 3.0 (FIN)
PWG 5100.3-2023: IPP Production Printing Extensions v2.0 (PPX)
PWG 5100.7-2023: IPP Job Extensions v2.1 (JOBEXT)
PWG 5100.11-2023: IPP Enterprise Printing Extensions v2.0 (EPX)
PWG 5100.13-2023: IPP Driver Replacement Extensions v2.0 (NODRIVER)
PWG 5100.14-2020: IPP Everywhere™ v1.1
  PWG 5100.20-2020: IPP Everywhere™ Printer Self-Certification Manual v1.1 (SELFCERT)
PWG 5100.15-2014: IPP FaxOut Service
PWG 5100.16-2020: IPP Transaction-Based Printing Extensions v1.1
PWG 5100.17-2014: IPP Scan Service
PWG 5100.18-2015: IPP Shared Infrastructure Extensions (INFRA)
PWG 5100.19-2015: IPP Implementor's Guide v2.0 (IG)
PWG 5100.22-2019: IPP System Service v1.0 (SYSTEM)
PWG 5101.1-2023: PWG Media Standardized Names 2.1
PWG 5102.4-2012: PWG Raster Format
Lines in RED have updates pending; lines in BLUE were ratified in the last 2 years

## Slide 5: Updates to Many Core IPP Specifications
IPP Finishings v2.0
IPP Production Printing Attributes v1.0
IPP Job Extensions v2.0
IPP Job and Printer Extensions – Set 2
IPP Job and Printer Extensions – Set 3
IPP Finishings v3.0
IPP Production Printing Extensions v2.0
IPP Job Extensions v2.1
IPP Enterprise Printing Extensions v2.0
IPP Driver Replacement Extensions v2.0

## Slide 6: PWG 5100.1-2022: IPP Finishings 3.0
Scope
Define IPP attributes to precisely describe finishing operations for both precise job settings and client preview, and to support monitoring the status of the Printer's finisher subsystems.
New and Updated Use Cases
Same use cases as IPP Finishings v2.1 / 2.0
New and Updated Features
Support for better client-side preview and constraints: "media-sheets-supported", "stitching-method", "punching-hole-diameter-configured", "stitching-angle"
Finisher supplies status and information: "printer-finisher-supplies" and "printer-finisher-supplies-description"
New multi-hole punching and engineering Z fold finishing types
Naming convention defined for site- or vendor-unique finishing templates

## Slide 7: PWG 5100.3-2023: IPP Production Printing Extensions v2.0 (1/3)
Scope
Define IPP attributes used for imposition, layout, and printing of covers, insert sheets, separator sheets, and different kinds of job sheets in high-volume "production" environments.
New and Updated Features
Support rotation as well as shifting of Finished Page Images
Printer indication of estimated time to Job processing start and completion
Client can now request when a Job needs to be completed
Client can force specified Input Pages to be imposed on front side of a Media Sheet
Client can specify how it wants the Impressions in a Job to be positioned, scaled, and rotated on one or more Media Sheets

## Slide 8: PWG 5100.7-2023 IPP Job Extensions v2.1 (1/3)
Scope
Defines the "media-col" Job Template attribute and extends the Job management, monitoring, and processing capabilities of IPP.
New and Updated Features
Printer can report the amount of time spent processing a Job
Client can report information about itself as well as any "upstream" software packages contributing to a Job Creation Operation
  New "client-info" replaces "document-format-details" (now deprecated / obsolete)
Job information counters for the number of pages, pages completed, impressions, and media sheets used
Granularly specify Job Template attributes a Printer must honor
  Like "ipp-attribute-fidelity" but more detailed
Ability to configure how the Printer manages a Job's Job Retention and Job History lifecycle phases
Support 'auto' selection for "print-content-optimize" and a 'virtual' input tray for "media-source"

## Slide 9: PWG 5100.11-2023: IPP Enterprise Printing Extensions v2.0 (1/2)
Scope
Defines new Job Release, Job Storage, Job Print Policy, Job Proof and Suspend, and Job Proof Print features to support printing workflows important to institutional IT environments such as corporate businesses, governments, and universities.
New and Updated Features
Job Print Policy feature
  New Get-User-Printer-Attributes operation provides Get-Printer-Attributes filtered for authenticated user
Job Proof and Suspend feature
  Provides a simpler proof printing solution more congruent with vendor proof printing implementations already in the marketplace for many years; replaces the legacy Job Proof Print feature, which is now DEPRECATED
Job Release feature
  Provides an updated system for authenticated Job release more comprehensive than the earlier Secure Print feature [PWG5100.11-2010] which was not interoperable with Job Proof and Suspend or Job Save and Reprint
Job Storage feature
  Defines a new system to create Stored Jobs for later reprinting, replacing the Job Save and Reprint feature [PWG5100.11-2010] which is now OBSOLETE
All the above features are designed to interoperate with one another, resolving a major design shortcoming of the previous version [PWG5100.11-2010]

## Slide 10: PWG 5100.13-2023: IPP Driver Replacement Extensions v2.0
Scope
Defines new attributes, values, and operations to support features, capabilities, localization, and status information that traditionally could only be provided by vendor- or model-specific drivers.
New and Notable Features
Job Presets – a way to group settings so they are applied as a set (adopted)
Modern "print-quality" replacement, based on an extension to "job-presets"
Message Catalog syntax extensions for "_tooltip" and "_helpurl" to enable localized tooltips and help content references to be provided by the Printer
Print Color Modes extended to support Printer-performed Job color transformations, including enabling client-side color transformation preview
A listing attribute naming site- or vendor-provided Job processing attributes to enable the Client to implement support for "expert controls" in a standard way
Overprinting for borderless printing

## Slide 11
Thank you for your time!